## Slide 1: Tolerating Hardware Device Failures in Software
Asim Kadav, Matthew J. Renzelmann, Michael M. Swift
University of Wisconsin-Madison
Notes: Thank you today I will be talking about Howto tolerate hardware device failures in software by making Making Linux drivers resilient to hardware crashes
20 mins including questsions

## Slide 2: Current state of OS-hardware interaction
Many Linux device drivers assume device perfection
  Common Linux network driver: 3c59x .c
While (ioread16(ioaddr + Wn7_MasterStatus))
& 0x8000)
;
Hardware dependence bug: Device malfunction can crash the system
HANG!
Notes: Operating systems communicate with hardware devices using drivers and many of these drivers assume device to behave properly.
For example If we look at a piece of code from a fairly common network driver, we can see that here that the driver code is reading a device register and waiting in an infinite while loop for it to be set to a particular value. If the device does not return the correct value, the system can hang indefinitely. HANG
We define such code instances as hardware dependence bugs where driver may crash the system when the device does not behave correctly

## Slide 3: Current state of OS-hardware interaction
void hptitop_iop_request_callback(...) {
arg = readl(...);
...
if (readl(&req->result) == IOP_SUCCESS) {
arg->result = HPT_IOCTL_OK;
}
}
Hardware dependence bugs present across driver classes
*Code simplified for presentation purposes
Highpoint SCSI driver(hptiop.c)
Notes: This figure shows another example of an hardware dependence bugs. The first line of the code reads in a pointer directly from the device. In the third line, marked as red, we can see that the pointer is dereferenced. If the read returns a corrupt value, the pointer de-reference can corrupt or crash the system. Such dangerous code is replete in the driver code base of Linux across
Driver classes and not just network and scsi drivers.

## Slide 4: How do the hardware bugs manifest?
Drivers often trust hardware to work correctly
    Drivers use device data in critical control and data paths
    Drivers do not report device malfunctions to system log
    Drivers do not detect or recover from device failures
Notes: And these hardware bugs, they manifest because driver code assumes that device will work as per its specifications.
More specifically, Drivers use device data to perform branching or while indexing kernel memory in critical ways as we saw in the two previous examples.
Drivers also tend to ignore minor device failures which either result in significant failures later on or appear at a much higher layer in software stack can waste considerable debugging time.
Also, since hardware is always assumed to work correctly and transient error free, often there are no provisions to detect or perform device recovery

## Slide 5: Carburizer
Goal: Tolerate hardware device failures in software through hardware failure detection and recovery
Static analysis tool - analyze and insert code to:
  Detect and fix hardware dependence bugs
  Detect and generate missing error reporting information
Runtime
  Handle interrupt failures
  Transparently recover from failures
Notes: To solve these problems, we built carburizer => a light-weight system to detect hardware failure and perform recovery
Consists of two components => a static analysis component to detect and fix hardware dependence bugs and missing error reporting information. This step
Produces a list of hardware dependence bugs and a optinally a binary with these problems fixed.
It also consists of a runtime component which can fix interrupt related failures and can also perform transparent online recovery.

## Slide 6: Outline
Background
Hardening drivers
Reporting errors
Conclusion
Notes: This is the outline of my talk

## Slide 7: Hardware unreliability
Sources of hardware misbehavior:
  Device wear-out, insufficient burn-in
  Bridging faults
  Electromagnetic radiation
  Firmware bugs
Result of misbehavior:
  Corrupted/stuck-at inputs
  Timing errors/unpredictable DMA
  Interrupt storms/missing interrupts
Notes: Hardware unreliability stems from the fact that modern CMOS devices prone to hardware failures.
Amongst common sources, errors occur due to device wear out and insufficient burn-in causing bit-flips, stuckats where single bit is flipped transiently or for extended times. There are also bridging faults where adjacent pair of bits are electrically mated producing an undesirable logical and or logical or.
Computers used in diverse environments so environmental conditions such as electro magnetic interference and radiations can cause hardware errors.
Modern embedded firmware have significant logic and bugs in them can cause problems like out of resource/memory leaks etc
(some devices have million lines of code in firmware)
As a result, these hardware problems cause errors which result in transient or extended corruption in driver inputs from device registers. They can also cause timing errors, stuck interrupt lines or unpredictable DMA in the driver.
----- Meeting Notes (9/2/11 14:34) -----
Discuss major reasons , we do not know what is common
electrical or mechanical failure
bugs in design or firmware
DMA
Talk about the result of the misbehavior
----- Meeting Notes (9/6/11 11:48) -----
Electronic problems
Design failure - Bugs in firmware, circuit design, specification bugs
Results of misbehavior: This means you get the same value if its stuck
what is timing ?? explain more talk about interrupts - This is important

## Slide 8: Vendor recommendations for driver developers
Recommendation | Summary | Recommended by |  |  | 
 |  | Intel | Sun | MS | Linux
Validation | Input validation |  |  |  | 
 | Read once& CRC data |  |  |  | 
 | DMA protection |  |  |  | 
Timing | Infinite polling |  |  |  | 
 | Stuck interrupt |  |  |  | 
 | Lost request |  |  |  | 
 | Avoid excess delay in OS |  |  |  | 
 | Unexpected events |  |  |  | 
Reporting | Report all failures |  |  |  | 
Recovery | Handle all failures |  |  |  | 
 | Cleanup correctly |  |  |  | 
 | Do not crash on failure |  |  |  | 
 | Wrap I/O memory access |  |  |  | 
Goal: Automatically implement as many recommendations as possible in commodity drivers
Notes: To address these problems, OSvendors lay out certain recommendations for driver developers on how to write driver code.
These can be classified in four broad classes.
First is Validate: Drivers should validate all input coming from the hardware
Second is Timing: Drivers should ensure all device operations occur in finite time and are synchronized with driver operations
Third is that drivers should appropriately report all device errors to the system administrator or system log.
Finally, the vendors also lay out certain guidelines on how drivers should perform device recovery.
The goal of our tool, carburizer is to automatically implement as many recommendations as possible.
MOVE BOX DOWN. Make automatically box
----- Meeting Notes (9/6/11 11:48) -----
Give example of validation, timing, reporting and recovery.

## Slide 9: Carburizer architecture
OS Kernel
If (c==0) {
.
print (“Driver init”);
}
.
.
Driver
Carburizer
If (c==0) {
.
print (“Driver init”);
}
.
.
Hardware dependency bug detection
Recovery and detection of interrupt issues
Hardened Driver Binary
Faulty Hardware
Carburizer Runtime
Kernel Interface
Compiler
List of bugs
Notes: To reiterate our solution, we perform static analysis on driver code during the build process to produce a kernel binary which checks hardware inputs and contains error reporting information.
The hardened kernel binary with the carburizer runtime ensures that driver can tolerate stuck interrupts or interrupt storms and also support online transparent recovery.
The resultant system consists hardened driver will detect a failure before corruption happens and trigger recovery The result is much more improved reliability against hardware device failures
----- Meeting Notes (9/6/11 11:48) -----
Produce a list of bugs and then it also produces list of bugs. compiler comes with second half of the picture

## Slide 10: Outline
Background
Hardening drivers
  Finding sensitive code
  Repairing code
Reporting errors
Conclusion
Notes: I will now talk about how we perform driver hardening

## Slide 11: Hardening drivers
Goal: Remove hardware dependence bugs
  Find driver code that uses data from device
  Ensure driver performs validity checks
Carburizer detects and fixes hardware bugs from
  Infinite polling
  Unsafe static/dynamic array reference
  Unsafe pointer dereferences
  System panic calls on non-debug path
Notes: The goal of carburizer here is to take a Linux driver and perform static analyses to detect and fix hardware dependence. Hardening a driver means to ensure that the driver sanitizes all input from device before using it in critical data or control paths.
If the driver does not perform this check, carburizer automatically inserts code that performs these checks and triggers a generic recovery service if the check fails.
In terms of the types of checks performed, Carburizer is able to find places in the driver where the system waits infinitely for device to enter a particular state or uses device data to perform unsafe array or pointer arithmetic. It also fixes code that invokes system panic when the driver is in an unexpected state - which is a common bad programming practice.
----- Meeting Notes (9/6/11 11:48) -----
Try to tie back to vendor recommendations - timing and valdiation

## Slide 12: Hardening drivers
Finding sensitive code
  First pass: Identify variables that contain data from the device
  We call them as tainted variables.
Notes: To find the sensitive code described in previous slide, carburizer does static analysis and performs these actions in two passes. The first pass is to identify tainted variables in the driver code. Tainted variables are those variables which contain data directly or indirectly originating from the devices and need to be checked.

## Slide 13: Finding sensitive code
First pass: Identify tainted variables
int test () {
a = readl();
b = inb();
c = b;
d = c + 2;
return d;
}
int set() {
e = test();
}
Tainted Variables
a
b
c
d
test()
e
Notes: I will show this with an example how we identify tainted variables.Carburizer consults a table of functions known to perform I/O such as readl for memory mapped I/O or inb for port I/O. Initially, carburizer marks all heap and stack variables that receive results from these functions as tainted.
Carburizer then propagates taint to variables that are computed from or are aliased to the tainted variables. We also propogate taint through return values.
The output of the first pass is a table containing all variables and functions that are tainted.
----- Meeting Notes (9/6/11 11:48) -----
Say what is second pass clearly (not propogation in second pass)

## Slide 14: Detecting risky uses of tainted variables
Second pass: Finding hardware dependence bugs
  Identify risky uses of tainted variables
Example: Infinite polling
  Driver waiting for device to enter particular state
  Solution: Detect loops where all terminating conditions depend on tainted variables
Notes: In the second pass, we use this table to find the risky uses of these variables.
As an example, one of the analyses in second pass consists of detecting control paths that wait forever for a particular input from the device. For each loop, carburizer computes the set of conditions that cause the loop to terminate through while clauses or conditional break, return or gotostatements. If all conditions are hardware dependent then the loop may iterate infinitely when the device misbehaves.

## Slide 15: Example: Infinite polling
Tainted variables used for critical timing decisions
static int amd8111e_read_phy(………)
{
...
reg_val = readl(mmio + PHY_ACCESS);
while (reg_val & PHY_CMD_ACTIVE)
reg_val = readl(mmio + PHY_ACCESS)
.
}
AMD 8111e network driver(amd8111e.c)
Notes: Here, we show a simple case detected by the tool, where the AMD network driver can hang the system if the device does not set the register
to a particular state.
While this is a simple example, our analysis can detect complex examples that are not obvious by eyeballing and may not be caught during manual code inspection. Examples of such code include loops with case statements or loops with nested function call

## Slide 16: Not all bugs are obvious
while (DAC960_PD_StatusAvailableP(ControllerBaseAddress))
{
DAC960_V1_CommandIdentifier_T CommandIdentifier= DAC960_PD_ReadStatusCommandIdentifier (ControllerBaseAddress);
DAC960_Command_T *Command = Controller ->Commands [CommandIdentifier-1];
DAC960_V1_CommandMailbox_T *CommandMailbox = &Command->V1.CommandMailbox;
DAC960_V1_CommandOpcode_T CommandOpcode=CommandMailbox->Common.CommandOpcode;
Command->V1.CommandStatus =DAC960_PD_ReadStatusRegister(ControllerBaseAddress);
DAC960_PD_AcknowledgeInterrupt(ControllerBaseAddress);
DAC960_PD_AcknowledgeStatus(ControllerBaseAddress);
switch (CommandOpcode)
{
case DAC960_V1_Enquiry_Old:
DAC960_P_To_PD_TranslateReadWriteCommand(CommandMailbox);
…
}
DAC960 Raid Controller(DAC960.c)
Notes: Here, we see a complex example where device read is called indirectly from these loops. It’s a really long loop with a switch statement thrown in at the end and its not very obvious looking at the code that it’s a hardware dependence bug. Carburizer can propagate taint via return values and can detect such bugs.
----- Meeting Notes (9/6/11 11:48) -----
Saying what the complexity is
talk about switch as well
explaining why its sensitive

## Slide 17: Detecting risky uses of tainted variables
Example II: Unsafe array accesses
  Tainted variables used as array index into static or dynamic arrays
  Tainted variables used as pointers
Notes: In the second pass, we also implement analyses to detect if any tainted variable or combination of tainted variable is used to perform unsafe array or pointer references.
When range of a device variable falls outside array bounds, or when dereferencing a random memory location, an incorrect reference can lead to reading an unmapped address or corrupt adjacent data structures.

## Slide 18: Example: Unsafe array accesses
Tainted variables used to index kernel memory w/o checks
static void __init attach_pas_card(...)
{
if ((pas_model = pas_read(0xFF88)))
{
...
sprintf(temp, “%s rev %d”,
pas_model_names[(int) pas_model], pas_read(0x2789));
...
}
Pro Audio Sound driver (pas2_card.c)
Notes: We can see here the driver reads in a variable from the device and uses it as an array index without any bounds check on the variable. This can crash the system if the memory refers to an unmapped address in the kernel. We now see the results

## Slide 19: Analysis results over the Linux kernel
Analyzed drivers in 2.6.18.8 Linux kernel
  6300 driver source files
  2.8 million lines of code
  37 minutes to analyze and compile code
Additional analyses to detect existing validation code
Re-ran analysis for 2.6.37.6 Linux kernel
Notes: We ran carburizer over the Linux 2.6.18 kernel driver tree. It analyzed and buil\t over 6300 driver source files consisting of over 2.8 million lines of code in 37 minutes. We try to detect hardware dependence bugs in as few code passes as possible.
We also detect existing validation code like timeout code in infinite loops, array bounds check and not-NULL checks. This is to improve the accuracy of our results.

## Slide 20: Analysis results over Linux 2.6.18.8
Found 992 bugs in driver code with 7.4% false positive rate (manual sampling of 190 bugs)
Driver class | Infinite polling | Static array | Dynamic array | Panic calls
net | 117 | 2 | 21 | 2
scsi | 298 | 31 | 22 | 121
sound | 64 | 1 | 0 | 2
video | 174 | 0 | 22 | 22
other | 381 | 9 | 57 | 32
Total | 860 | 43 | 89 | 179
2.6.37.6 | 1164 | 55 | 156 | 214
Notes: This table shows the results of our analysis on Linux kernel across different driver classes. Overall, we are able to find approximately 992 bugs at the false positive rate of 7.4%. While we implement analyses to detect false positives, some false positives remain because some drivers performed validation differently. For e.g. some drivers perform timeout validation in a different function called from within the loop. There may also be more bugs in the drivers because carburizer tracks taint by function return variables but not via procedure arguments.
The results suggest that modern drivers can do a better job of avoiding hardware bugs and are susceptible to crashes in the face of transient hardware failures. Carburizer can detect these hardware dependence bugs for the developer.
Finding bugs is valuable but reliability does not increase until the bug is fixed.
On 2.6.37.6, found 1064 polling, 200 array dereference and 200 panic calls
----- Meeting Notes (9/6/11 11:48) -----
Make bolder bar for 2.6.37.6
driver could do a better job instead of poor job

## Slide 21: Repairing drivers
Hardware dependence bugs difficult to test
Carburizer automatically generates repair code
  Inserts timeout code for infinite loops
  Inserts checks for unsafe array/pointer references
  Replaces calls to panic() with recovery service
  Triggers generic recovery service on device failure
Notes: This is important because the hardware dependance bugs occur infrequently and cannot be detected via regular stress testing. Hence, carburizer also fixes the detected bugs automatically.
To fix these bugs, for example, the infinite loops, we insert time out code long enough for any device to respond. For unsafe array references, when array bounds can be determined statically, carburizer computes them and inserts a suitable bounds check. For dynamic arrays bounds and pointers valid values are not known but carburizer inserts a not-NULL check. When any of these checks fail, carburizer invokes a generic recovery service
----- Meeting Notes (9/6/11 11:48) -----
what is key point??
Talk about shadow drivers
Make second line the second bullet
Given this ability to recover at any point...Replace calls to panic to calls to shadow drivers

## Slide 22: Outline
Background
Hardening drivers
Reporting errors
Conclusion
Notes: 16:25

## Slide 23: Reporting errors
Drivers often fail silently and fail to report device errors
  Drivers should proactively report device failures
  Fault management systems require these inputs
Driver already detects failure but does not report them
Carburizer analysis performs two functions
  Detect when there is a device failure
  Report unless the driver is already reporting the failure
Notes: On many occasions drivers fail silently and do not report device errors. But OS and hardware vendors recommend monitoring hardware failures to allow proactive device repair or replacement. For example, the Solaris Fault Management architecture feeds error reported by device drivers into a diagnosis engine and recommends a high level action such as replacing or disabling a device.
The goal of carburizer here is to detect conditions in the driver where there is a device failure. And to add a reporting statement unless driver is already reporting these failures

## Slide 24: Detecting driver-detected device failures
Detect code that depends on tainted variables
  Perform unreported loop timeouts
  Returns negative error constants
  Jumps to common cleanup code
while (ioread16 (regA) == 0x0f) {
if (timeout++ == 200) {
sys_report(“Device timed out %s.\n”, mod_name);
return (-1);
}
}
Reporting code added by Carburizer
Notes: To insert reporting statements at places where the driver already detects device failures – Carburizer implements analyses to detect code paths which timeout from a loop due to a device error or return a negative error constant due to a device error. Carburizer also inserts error reporting information where driver jumps to common cleanup code due to a device error.
For example – in the code snippet shown here, the driver correctly detects a timeout loops but does not report it. Carburizer correctly inserts a reporting statement. Carburzier does not insert reporting statements if the driver already reports device failures.
----- Meeting Notes (9/6/11 11:48) -----
hyphen between driver and detected

## Slide 25: Detecting existing reporting code
Carburizer detects function calls with string arguments
static u16 gm_phy_read(...)
{
...
if (__gm_phy_read(...))
printk(KERN_WARNING "%s: ...\n”, ...);
Carburizer detects existing reporting code
SysKonnect network driver(skge.c)
Notes: Carburizer also detects existing reporting information implemented in the original driver by looking for calls to functions that contain string messages as arguments. As we can see here in this example…

## Slide 26: Evaluation
  Fixed 1135 cases of unreported timeouts and 467 cases of unreported device failures in Linux drivers
  Evaluation: Manual analysis of drivers of different classes
  No false positives
Driver | Class | Carburizer reported/Driver detected device failures
bnx2 | network | 17/24
mptbase | scsi | 17/28
ens1371 | sound | 9/10
Carburizer automatically improves the fault diagnosis capabilities of the system
Notes: To evaluate our error reporting techniques, we resorted to manual analysis of the code generated by carburizer and compared the actual device errors vs reported errors.
While there are no false positives, carburizer is able to detect most errors and miss few ones. These false negatives exist due to the fact that drivers detect device errors but ignore them and do not return negative error constants or flag them in any fashion. Also, in few cases error values are returned by out parameters which the analysis of carburizer does not track.
Overall, carb. detected and fixed a total of 1600 unreported device failures. Many of these are low level device errors which if not reported will make it difficult for the administrator to nail down the problem in the system. Carburizer improves fault diagnosis by promptly detecting these failures.
----- Meeting Notes (9/6/11 11:48) -----
Put 1135 result first instead of vice versa
driver-detected
title in third coloumn is not clear

## Slide 27: Conclusion
Recommendation | Summary | Recommended by |  |  | 
 |  | Intel | Sun | MS | Linux
Validation | Input validation |  |  |  | 
 | Read once& CRC data |  |  |  | 
 | DMA protection |  |  |  | 
Timing | Infinite polling |  |  |  | 
 | Stuck interrupt |  |  |  | 
 | Lost request |  |  |  | 
 | Avoid excess delay in OS |  |  |  | 
 | Unexpected events |  |  |  | 
Reporting | Report all failures |  |  |  | 
Recovery | Handle all failures |  |  |  | 
 | Cleanup correctly |  |  |  | 
 | Do not crash on failure |  |  |  | 
 | Wrap I/O memory access |  |  |  | 
Notes: To summarize, vendors recommend driver developers to consider the significant hardware unreliability in practice. However, incorporating a feature that does not affect functionality or is captured by stress testing is easy to miss.

## Slide 28: Conclusion
Recommendation | Summary | Recommended by |  |  |  | Carburizer Ensures
 |  | Intel | Sun | MS | Linux | 
Validation | Input validation |  |  |  |  | 
 | Read once& CRC data |  |  |  |  | 
 | DMA protection |  |  |  |  | 
Timing | Infinite polling |  |  |  |  | 
 | Stuck interrupt |  |  |  |  | 
 | Lost request |  |  |  |  | 
 | Avoid excess delay in OS |  |  |  |  | 
 | Unexpected events |  |  |  |  | 
Reporting | Report all failures |  |  |  |  | 
Recovery | Handle all failures |  |  |  |  | 
 | Cleanup correctly |  |  |  |  | 
 | Do not crash on failure |  |  |  |  | 
 | Wrap I/O memory access |  |  |  |  | 
Carburizer improves system reliability by automatically ensuring that hardware failures are tolerated in software
Notes: We presented Carburizer – a reliability tool which implements the recommendations which do not require any semantic information about the device or any hardware support. To conclude, carburizer improves system reliability by automatically implementing vendor recommendations and tolerating hardware device failures in software.

## Slide 29: Thank You
Contact for driver verification/tool access
  kadav@cs.wisc.edu
Details on carburizer
  http://cs.wisc.edu/~kadav/carb/
OS Kernel
If (c==0) {
.
print (“Driver init”);
}
.
.
Driver
Carburizer
If (c==0) {
.
print (“Driver init”);
}
.
.
Hardware dependence bug detection
Recovery and detection of interrupt failures
Hardened Driver Binary
Faulty Hardware
Carburizer Runtime
Kernel Interface
Compiler